## Slide 1: Computer Networks
By Shailesh Kumar Khanchandani

## Slide 2: Topics Covered
Transport Layer – Services, Flow and Congestion Control Protocols.
Datagrams & UDP – Services & Applications.
TCP – Services, Features, States, Ports and Sockets.
Session and Application Layer – Introduction to FTP, TELNET, SSH and SNMP.
Overview of Wireless Communication
Adhoc Networks and Tethering.

## Slide 3: Transport Layer
The transport layer, layer 4 in the OSI model, provides process-to-process communication between applications on different devices. It offers several key services:
  Process-to-Process Delivery: Ensures data reaches the correct application on the destination device.
  Reliability: (Implemented by TCP) Guarantees in-order and error-free delivery of data.
  Flow Control: Regulates the data flow between sender and receiver to prevent overwhelming the receiver. (Implemented by both TCP and UDP)
  Congestion Control: (Implemented by TCP) Helps prevent network congestion by dynamically adjusting the data transmission rate.

## Slide 4: Flow Control and Congestion Control Protocols
  Flow Control:
  Stop-and-Wait: Sender transmits a packet and waits for an acknowledgment (ACK) before sending the next. Simple but inefficient for large data transfers.
  Sliding Window: Sender transmits multiple packets within a window and waits for ACKs before sending the next window. More efficient than stop-and-wait.
Congestion Control Protocols:
  TCP Congestion Control: Employs techniques like slow start, congestion avoidance, and fast retransmit to dynamically adjust the transmission rate based on network congestion signals.

## Slide 5: Datagrams
Datagrams are self-contained units of data used for communication over networks. They act like individual postcards containing:
  Header: This section includes information for routing the datagram, such as the sender's and receiver's IP addresses and port numbers (if applicable).
  Payload: This is the actual data being sent, which could be application data, control information, or anything else requiring transmission.
  Think of datagrams as individual packages delivered by a mail carrier. Each package has an address label (header) specifying the sender and recipient, and the contents inside (payload) is the actual message or item being delivered.

## Slide 6: UDP (User Datagram Protocol)
UDP is a transport layer protocol that utilizes datagrams for communication. It offers several key characteristics:
  Connectionless: Unlike connection-oriented protocols like TCP, UDP doesn't establish a connection before sending data. This makes it faster and simpler.
  Unreliable: UDP doesn't guarantee delivery, in-order arrival, or error checking of datagrams. It simply sends them off and hopes for the best.
  Fast: Due to the lack of connection setup and overhead, UDP is faster than TCP for applications where speed is a priority.
  Low Overhead: UDP has a simpler header structure compared to TCP, leading to lower processing requirements on sending and receiving devices.

## Slide 7: Applications of UDP
UDP's speed and simplicity make it suitable for specific applications where:
  Real-time data delivery is crucial: In applications like online gaming and video streaming, a slight delay or data loss might be tolerable compared to the benefits of real-time updates.
  Error correction is handled at the application level: Applications can implement their own error checking and retransmission mechanisms if necessary.
  Data loss is acceptable: For applications like live audio or video broadcasts, occasional dropped packets might not be critical, and the benefits of faster transmission outweigh the drawbacks.

## Slide 8: Applications of UDP
Here are some common UDP applications:
  Online Gaming: UDP allows for fast updates on game state information between players.
  Video Streaming: UDP enables real-time video transmission, even if some packets are lost.
  Voice over IP (VoIP): UDP facilitates real-time voice communication, where occasional dropped packets might result in a slight stutter but wouldn't disrupt the entire conversation.
  DNS (Domain Name System) Lookups: UDP is used for quick DNS queries to translate domain names to IP addresses.
In summary, datagrams provide the basic units of data transfer, and UDP leverages them for fast and lightweight communication in applications that prioritize speed over guaranteed delivery.

## Slide 9: TCP (Transmission Control Protocol)
TCP is a connection-oriented transport layer protocol that offers reliable and ordered data delivery over networks. It's the workhorse protocol for many internet applications that require accurate data transfer, like file downloads, email, and web browsing.
Here's a breakdown of TCP's key aspects:
Services:
  Reliable Delivery: TCP guarantees in-order and error-free delivery of data packets. It achieves this through:
  Sequence numbers: Assigns a unique number to each packet, ensuring they arrive in the correct order.
  Checksum: Calculates a checksum for each packet to detect transmission errors.
  ACK/NACK mechanism: Sender receives acknowledgments (ACKs) for successfully delivered packets and requests retransmission of lost or corrupted ones (NACKs).

## Slide 10: TCP (Transmission Control Protocol)
Flow Control: Regulates the data flow between sender and receiver to prevent overwhelming the receiver's buffer.
Congestion Control: TCP dynamically adjusts the transmission rate to avoid network congestion.
Features:
Three-way handshake: Establishes a connection between sender and receiver before data transmission. This ensures both parties are ready to communicate.
Sliding Window: Sender transmits multiple packets within a window and waits for ACKs before sending the next window. This improves efficiency over stop-and-wait flow control.

## Slide 11: States
A TCP connection goes through different states throughout its lifecycle:
LISTEN: Server waits for a connection request.
SYN_SENT: Client sends a connection request (SYN).
SYN_RECEIVED: Server acknowledges the request (SYN-ACK).
ESTABLISHED: Data transfer can occur.
FIN_WAIT_1: Client initiates connection termination (FIN).
CLOSING (or LAST_ACK): Server acknowledges termination (ACK) and sends its own termination (FIN).
TIME_WAIT: Sender waits for a certain time to ensure all packets are received by the receiver before closing the connection.
CLOSED: Connection is closed on both sides.

## Slide 12: Ports and Sockets
TCP uses port numbers to identify different applications on a device. Each application registers with the operating system and is assigned a port number. When a TCP segment (containing data) arrives, the port number in the header helps the operating system deliver the data to the correct application. Well-known ports are pre-assigned for specific services (e.g., port 80 for HTTP traffic).
A socket is a combination of an IP address and a port number. It uniquely identifies an endpoint (application) on a network. Think of a socket like a specific mailbox at a post office - the combination of the address and mailbox number directs mail to the intended recipient. Applications use sockets to send and receive data over TCP connections.
In essence, TCP provides a reliable communication channel for applications that require guaranteed data delivery. By establishing connections, utilizing sequence numbers, error checking, and flow control mechanisms, TCP ensures your data arrives at its destination accurately and in order.

## Slide 13: Session and Application Layer – Introduction to FTP, TELNET, SSH and SNMP.
The upper layers of the OSI model deal with application-specific communication and data presentation.
Session Layer (Layer 5): Manages sessions between applications, including connection establishment, data exchange, and termination. This layer is often transparent to users but plays a crucial role in coordinating communication flow between applications. (e.g., RPC - Remote Procedure Call)
Presentation Layer (Layer 6): Deals with data formatting and presentation between applications. It can handle tasks like data encryption/decryption, character set conversion, and compression to ensure compatibility between different systems.
Application Layer (Layer 7): Provides network services directly to users. This is the layer where familiar applications like web browsers, email clients, and file transfer tools interact.

## Slide 14: Here's an introduction to some common Application Layer protocols:
FTP (File Transfer Protocol):
Used for transferring files between computers on a network.
Offers two connection modes:
  Passive Mode: Client initiates data connection, suitable for firewalled environments.
  Active Mode: Server initiates data connection, simpler but might be blocked by firewalls.
Common uses: Downloading files, uploading website content, file backups.
Telnet:
Provides remote terminal access to another computer.
Users can log in to a remote machine and interact with its command-line interface.
Considered less secure due to unencrypted data transmission. (Replaced by SSH for secure remote access)

## Slide 15
SSH (Secure Shell):
Secure alternative to Telnet that encrypts data transmission.
Provides secure remote login and command-line access.
Widely used for server administration, secure file transfer, and secure remote access to applications.
SNMP (Simple Network Management Protocol):
Used for network management and monitoring.
Enables devices to exchange information about their status, configuration, and performance.
Essential for network troubleshooting and performance optimization.

## Slide 16: Overview of Wireless Communication
Wireless communication refers to the transmission of information over a distance without using physical cables or wires. It has revolutionized the way we connect and interact with the world, enabling a vast array of applications. Here's a breakdown of the key concepts:
Transmission Medium: Unlike wired communication that uses cables (coaxial, fiber optic), wireless communication utilizes electromagnetic waves (radio waves, microwaves, infrared) to carry data. These waves propagate through the air, eliminating the need for physical connections.

## Slide 17: Overview of Wireless Communication
Technologies: Various technologies facilitate wireless communication, each with its own characteristics:
  Cellular Networks: Provide mobile internet access through a network of radio towers and base stations. Phones connect to nearby towers for data transmission.
  Wi-Fi (Wireless Fidelity): Enables local area network (LAN) connections using radio waves. Commonly used for internet access within homes, offices, and public hotspots.
  Bluetooth: Short-range wireless technology for connecting devices like headsets, printers, and smartphones for data exchange or audio streaming.
  Satellite Communication: Uses satellites orbiting the Earth to transmit data over long distances. Ideal for remote areas where terrestrial infrastructure is limited.

## Slide 18
Advantages of Wireless Communication:
Mobility: Enables us to connect and access information from anywhere with a wireless signal.
Scalability: Wireless networks can be easily expanded to accommodate additional devices without complex cabling.
Cost-effective: Eliminates the need for extensive cable infrastructure, reducing installation and maintenance costs.
Convenience: Provides greater flexibility and freedom of movement for users.
Disadvantages of Wireless Communication:
Security: Wireless signals are susceptible to interception compared to wired connections. (Encryption is crucial)
Range Limitations: The range of wireless signals can be affected by factors like distance, obstacles, and interference.
Reliability: Wireless connections can be impacted by environmental conditions or network congestion.

## Slide 19: Applications of Wireless Communication
Mobile internet access (cellular networks, Wi-Fi)
Bluetooth devices (headsets, speakers)
Satellite communication (navigation, remote internet access)
Smart home devices (thermostats, security systems)
Wireless sensors (industrial automation, environmental monitoring) The future of wireless communication is constantly evolving with advancements in technologies like 5G and beyond, promising even faster speeds, wider coverage, and improved reliability.

## Slide 20: Ad-Hoc Networks and Tethering
Both ad-hoc networks and tethering allow devices to connect and share resources wirelessly, but they differ in their setup and purpose:
Ad-Hoc Networks:
Definition: A temporary network created by devices connecting directly to each other without a central access point (router). Think of it like a group conversation where everyone can talk to everyone else directly.
  Setup: Devices participating in the ad-hoc network need to be configured with the same network name (SSID) and security settings (optional) to establish connections.
  Functionality: Devices within the ad-hoc network can share files, printers, or play multiplayer games directly.

## Slide 21
Limitations:
  Typically smaller range compared to networks with a router.
  Security can be a concern if not properly configured.
  Not suitable for internet access sharing unless one device in the network has a pre-existing internet connection that can be shared with others (tethering).
  Example: A group of friends creating an ad-hoc network to play multiplayer games on their laptops in a park.
Tethering:
Definition: Using a mobile device (smartphone or mobile hotspot) to share its internet connection with other devices like laptops or tablets. It's like turning your phone into a portable Wi-Fi router.
Methods: Tethering can be done through various methods depending on the device:
  Wi-Fi hotspot: Most common method, creates a Wi-Fi network that other devices can connect to using the phone's SSID and password.
  USB tethering: Connects the mobile device to another device using a USB cable, sharing the internet connection.
  Bluetooth tethering: Shares the internet connection via Bluetooth, but typically slower than Wi-Fi.

## Slide 22
Benefits: Provides internet access to other devices on the go, useful for travel or situations where Wi-Fi isn't available.
Limitations:
May incur data charges depending on your mobile plan.
Can drain the battery of the tethering device.
Choosing Between Ad-Hoc Networks and Tethering:
If you just need to share files or play games directly between devices without internet access, an ad-hoc network might be sufficient.
If you need to provide internet access to other devices from your mobile connection, tethering is the way to go.